## Slide 1
30 VL53L0X Infra-Red Laser Time-of-Flight distance sensors
  Small form factor
  1.2m range
  30ms measurement time
  20mW power consumption each
JSN-SR04T ultrasonic distance sensor
  5m range
  40ms measurement time
  Waterproof sensor enclosure
A
JSnJSasdjflk;
8 C0820B002F Haptic Feedback Motors
  Small form factor
  Low power consumption
  Highly adjustable intensity level
HC-05 Bluetooth Modules
Arduino Pro-Mini Microcontrollers
6600 mAh Li-Ion Batteries
Student-designed PCBs and Enclosures
System Overview
System takes in sensor data locating nearby objects in 360° from a headband of several types of sensors.
Sensor data is transferred wirelessly to a waistband of haptic feedback vibration motors, which are spread evenly around the band.
Haptic feedback motors vibrate with intensity corresponding to nearest object distance in that direction.
Navigation assistance
for the vision impaired
A wearable system that translates visual information into tactile feedback.
requirements
Minimum 12 hr battery life.
Battery will charge in less than 15 hrs.
9/10 users will determine the distance to an object with an accuracy of 1 m for objects within 5 m in front of the user, and 20cm for objects within 1 m in any direction.
Optional low-power mode with minimum 24 hr battery life, at the cost of 100 ms additional response time.
9/10 blindfolded users will turn into a doorway at the end of a 20 m long hallway without touching the walls.
Detected object direction is indicated to within 30°.
System feedback responds to changes in object position in less than 200ms.
Spraying 100mL of water over the entire system in two minutes will not damage the system.
The system weighs less than 900g, and after 15 minutes of use, 9/10 users report the system is comfortable.
Wireless connection between the sensor and feedback bands remain uninterrupted for 12 hours.
Ece #34
Key technologies Used
Team Members
Jacy Barr(right) (barrja@oregonstate.edu)
  Project Management
  Harnesses and Enclosures
  Haptic Feedback Modules
Samuel Lee(center) (leejiaks@oregonstate.edu)
  Bluetooth Communication
  Microcontrollers and Code
Sean Sylwester(left) (sylwests@oregonstate.edu)
  Ultrasonic and IR Distance Sensors
  Power Supply
  PCBs
Block Diagram
Object Distance
and Direction
Sensor Controller
Power
Ultrasonic Sensor
Laser Sensors
Power Supply
3.3V
Haptic Feedback
Feedback Controller
3.3V
3.3V
Vibrations
3.3V
3.3V
3.3V
Object Detection Ranges
Green: Ultrasonic Sensor
Red: Laser ToF Sensors
PROJECT MOTIVATION
253 million people worldwide live with vision impairment
36 million people are completely blind.
The White Cane has some significant drawbacks:
Difficult to use indoors and in crowded areas
Misses objects above waist-height
Other assistive technologies have problems as well:
Expensive
Uncomfortable
Unresponsive
Poor battery life
Not waterproof
Our system seeks to address the shortcomings of the White Cane while avoiding common pitfalls of other assistive technologies.
1
2
3